Lesson Title Science – Material resiliency

Standard Course of Study Objectives

Goal 1 The learner will design and conduct investigations to demonstrate an

understanding of scientific inquiry.

2.03   Evaluate technological designs for application of scientific principles.

Risk and benefits, constraints of design and consistent testing

protocols.

Science Background information

Expert information in this section has been provided by:

Rolin E. Barrett, Jr., Ph.D., P.E.

Consulting Engineer and Accident Reconstruction Specialist

Barrett Engineering

Eric Klang, Ph.D.

Director, Undergraduate Program

Mechanical & Aerospace Engineering

Faculty Advisory, Wolfpack Motorsports

Expert:	In passenger cars the beginning of occupant protection was to

basically make the passenger compartment safer beginning with

the windows, windshield, and that kind of thing.  That kept out

road debris and kept birds from flying into your face while you

were driving - laminated glass has saved thousands of lives.

Later, cars had padded dashboards and low profile knobs and

handles to protect passengers when they were thrown around

the inside of the car during an accident.  At about the same

time seatbelts became available.  Designs that allowed the

chassis to deform during an impact began to appear.  As

vehicles became safer new problems were uncovered.  Not

everyone used seatbelts and often those who did sustained

injuries that the seatbelt could not avoid.  Airbags were

introduced to address these problems

The safety equipment is often designed for one severe

accident.  But sometimes that safety equipment can be damaged

or consumed in a small accident.  If an accident is severe it may

cause a high-rate load to be applied to the seatbelt system.

And so the seatbelt system may be weakened.  They may have

damaged the fibers of the seatbelt in a severe enough accident.

But consider that a large heavy driver is going to load that

seatbelt more than a small lightweight driver.  So a small

accident involving a heavy driver or heavy passenger could

actually compromise that system at a much earlier value than

for a small light driver or passenger in the same situation.

Interviewer:    	Would you say that one of the big differences between a

race  car and a private car would be seatbelt use?

Expert:         Yes I would.  Seatbelt usage among professional drivers is 100

percent.  They know from both experience and from their

training that the seatbelt will save their life more often than

not.  The seatbelt is the one device that is most likely to help

them out during an accident.  An airbag is a device that can

offer some improvement for the types of accidents where it’s

designed to deploy.  You really find the seatbelt is again the

most efficient general use device for safety but you do have to

use it properly.

Interviewer:	What is the ultimate restraint system for safety in passenger vehicles?

Expert:        Currently the best restraint systems available in vehicles are a

combination of seatbelts and air bags.  The seatbelt is a good

basic restraint.  It holds you in place.  The air bag works for

certain scenarios.  Each air bag is devised for a given type of

accident.  So they’re more specific.  They’re not a general

device.  The seatbelt is truly the most general device.

Interviewer:	Ok.  How do these two differ from the optimum system?

Expert:        We would like to have people packaged in cars like we package

eggs for transport.  But it’s not practical to do that.  So we

have to find something that blends in with every day needs.

And the current system of seatbelts and airbags do an

excellent job.  For the near future we’ll see an expansion of the

airbag concept to cover other types of accidents than have

previously been covered.  We’ve seen them go from a simple

head-on type of protection to side protection and now rollover

protection.  I think we’ll see some small extensions of that.  And

we’ll also see the electronics, which activate the airbag systems

to be more precisely controlled for each specific accident

scenario.

Interviewer:	Will airbags eventually be found in NASCAR?

Expert:       One thing we can expect is to see multiple-use airbags.  If you’re

hit in a collision and then another vehicle comes along seconds

or minutes later and collides with you, you’re protected.

Interviewer:	You say though that one of the big differences between a race car and a private car would be seatbelt use?  The race drivers know the seatbelts save lives.  So that system works.  The reason we have airbags in passenger cars is that people did not use their safety belts

Expert:         Yes I would.  Seatbelt usage among professional drivers is 100

percent.  They know from both experience and from their

training that the seatbelt will save their life more often than

not.  The seatbelt is the one device that is most likely to help

them out during an accident.  Airbag is a device that can offer

some improvement for the types of accidents where it’s

designed to deploy.  But you really find the seatbelt is again the

most efficient general use device for safety.

National Science Standards

-All students should develop abilities necessary to do scientific

inquiry and understandings about scientific inquiry.

-All students should develop an understanding of properties and

changes of properties in matter, motions and forces and

transfer of energy.

-All students should develop abilities of technological design and

understandings about science and technology.

-All students should develop understanding of science and

technology in society.

Teacher Lesson Plans

Lab: The students will be expected to test their hypothesis of which fabric will be the most suitable for a safety harness

Student expectation: In teams, students will prepare a pattern 2 inches wide by 18 inches long. Select fabrics for testing. Pin and cut to the pattern. The students will measure the initial length as well as length following the addition of one-half gallon of water and one gallon of water. Care should be taken to also measure the length after removal of each weight treatment. The students will be expected to compare their data with other groups and prepare a report that will illustrate their findings and conclusions.

Hints:  Students may bring in old clothes or blankets.  The key is the strips of fabric need to be consistent.   Creating a 2 inch by 18 inch pattern of cardstock for each group would increase consistency.  Students will need 2 strips of three different fabrics.  (6 strips in total).  Fabric remnants from this experiment may be used in the flame retardancy lab.

Materials List

Different kinds of fabrics

Gallon and half-gallon container with screw cap and a handle for each group

String (1 yard) for each group

Yardstick

Heavy duty spring clamps

20” 1X4 piece of wood per group (to be placed between two desks)

water

pins & newspaper for patterns

sewing scissors

Student Worksheets

Name ________________		Materials Resiliency Lab

Names of others in your group ________________________

Write down a description of each piece of fabric:

Read through the procedure.  Before conducting the lab, hypothesize what will happen to each of the pieces of fabric.    Compare your prediction with the predictions of the other members of your group.

Procedure:

1)	Cut 2 strips of 3 different fabrics.  Each strip needs to be 2” x 18”.  Use a template to be sure all pieces are the same size.  Precise cutting is important for this lab.

2)	Set up the 20” 1 x 4 piece of wood.  Move two desks close enough and place the piece of wood so an end is on each desk.  The fabric will be clamped onto this piece of wood.

3)	Fill the half-gallon jug with water.  Select one piece of fabric. Loop the fabric through the handle of the jug.  Clamp the ends of the fabric onto the piece of wood.

4)	Use the string to measure the stretched fabric.  Before removing the clamps and the jug, take the piece of string and mark the length of the fabric on the string.	Use the yardstick to measure that length.  Record results.

5)	Take the second strip.  Fill the gallon jug with water.  Repeat the steps.  Record results.

6)	Continue these same steps for the two remaining fabrics.

|  | Fabric 1 Description: | Fabric 2 Description: | Fabric 3 Description: |
| --- | --- | --- | --- |
| ½ gallon measurement: |  |  |  |
| 1 gallon measurement: |  |  |  |

Compare the actual results with your earlier predictions.

Assessment/Checking for Mastery:

Name ___Teacher Edition________         Quiz – Materials Resiliency Lab

1)	In selecting materials for seat belts, list two pieces of information you learned

during the lab that would help you better select safe materials.

(Possible answers:

- Whichever fabric had the greatest stretch (flannel, knit) would have stretched too much.   If seat belts stretch too much, the person will fly forward.

- An item that stretches too little can also be dangerous to the body in an accident causing injury where it comes in contact with the body.)

2)	If you were assigned to create the cord for an amusement park bungee jump, what

are two components of the bungee cord that would be important for rider safety?

(Possible answers: stretch so there isn’t a sudden stop for the rider

Strength so that the cord doesn’t snap and break

Quantity of stretch so rider doesn’t hit the ground

That the stretch of the cord doesn’t increase with repetitive use so rider doesn’t hit the ground)

Name _______________________         Quiz – Materials Resiliency Lab

1)	In selecting materials for seat belts, list two pieces of information you learned

during the lab that would help you better select safe materials.

2)	If you were assigned to create the cord for an amusement park bungee jump, what

are two components of the bungee cord that would be important for rider safety?