Lesson Title -Technological Design – self-propelled car

Standard Course of Study Objectives:

Goal 1 The learner will design and conduct investigations to demonstrate an

understanding of scientific inquiry.

2.02   Use information systems to identify scientific needs, human needs or

problems that are subject to technological solution.

2.03   Evaluate technological designs for application of scientific principles,

risk and benefits, constraints of design and consistent

testing protocols.

4.04	Describe the suitability of materials for use in technological design

Science Background information –

Expert information in this section has been provided by:

Rolin E. Barrett, Jr., Ph.D., P.E.

Consulting Engineer and Accident Reconstruction Specialist

Barrett Engineering

Eric Klang, Ph.D.

Director, Undergraduate Program

Mechanical & Aerospace Engineering

Faculty Advisory, Wolfpack Motorsports

Interviewer:		How is energy used in a car?

Expert:		Some of the energy may be used to heat or cool the

interior of the vehicle by the air conditioner or the

heater.    S a little bit goes there.   Some of the other

energy is used in other ways such as electrical energy to

operate systems within the car, power seats, radios,

sunroof, windows, that kind of thing.   Most of the energy

is used to rotate the wheels.

Interviewer:		The engine converts chemical energy into kinetic energy.

Does the engine use energy during this process?

Expert:		Yes.   Some of the energy goes back into operating the

mechanisms of the engine as well as the drive train.  One

other thing to consider is that when you’re driving and

you come up to a stop sign or stoplight or simply want to

slow down you take some of the energy of motion, the

kinetic energy and convert that to heat energy using

friction, the brakes.   Some vehicles are designed to

recoup some of the energy that would otherwise be lost

during braking.  These vehicles sometimes are said to

have a regenerative feature.  For example an electric

vehicle upon braking may allow the motors to operate as

generators and to take some of that energy of motion

and put it back to the energy storage device – the

battery.   This is done in some of the newer vehicles,

hybrids and such to allow better economy.

Interviewer:		What can be done to increase the efficiency of an

engine?   That is, how can we convert more of the

chemical energy into kinetic energy?

Expert:		Some vehicles may use an inner cooler to take heat out of

the air to increase the density of the air charge into the

engine.   This improves efficiency.   Other vehicles may

use a super charger or turbo charger to extract some of

the energy from the engine and place it into the form of

better packing air for the combustion into the engine.  In

the case of the turbo charger, they’re specifically taking

energy that would be lost through the tailpipe, through

the heat of the engine, the exhaust leaving.   They take

this waste energy and put it back.

There’s another type of device which is similar to a turbo 	charger and sometimes called a scavenger.  Slang terms.

But this device is basically like half of a turbo charger

with the shaft.   And it takes some of that energy from

the exhaust and mechanically returns it.  We hear a lot

of stores over the years about the miracle carburetor or

miracle fuel injection system or some special engine that

will somehow allow the vehicle to attain this wonderful

mileage.   Usually the stories tell of some vehicle that will

get 300 miles to the gallon or something such as this.  If

someone could invent this they would be very wealthy,

they would be very popular in society.  The reality is

there’s only so much air you can extract from our fuels.

Gasoline only holds so much energy per gallon.   The same

is true with diesel fuel.  They have a limited amount of

energy.  And engineers do strive to extract as much as

possible.  But there’s no great conspiracy to hide the use

of energy.

Interviewer:		Describe design factors that enhance speed versus

design factors that enhance distance.

Expert:		Dragsters may be fun but it’s hard to go to the beach or

take your groceries home in them.   So we know that

design factors definitely will allow a vehicle to be fast or

achieve great distance.  And we can see that in cars

currently available.  A high performance sports car

offers the potential for great speed.   Family cars and

vans offer better mileage.

We have to be careful though when we strive to design

something that is a mater of all situations because

frequently the compromise will give a vehicle that will do

none of these very well.    So we want to focus on the

areas that are important to us.  If it happens to be speed

or distance then we need to focus on one and not so much

focus on the other.

Interviewer:		Several types of fuel are available.  One general

distinction is the nature of the fuel – solid, liquid or gas.

Please discus the pro’s and con’s of some examples.

Expert:		Solid fuels are considered more stable than liquid fuels.

Sold fuel vehicles have been produced.  Examples include

wood burning trains up until the nineteenth century and

coal burning trains that were used later, well into the

twentieth century.  And there have been some

experimental cars that used a very finely powdered coal.

They powdered the coal to make it more than coal.  And

they were able to move it through the fuel system.  But

these have never achieved commercial success.

We use gasoline because it’s fairly cheap.  Additionally

the infrastructure is in place for gasoline which is a huge

savings.   Look at going to hydrogen.   The infrastructure

is a real concern.   We have hydrogen powered rocks by

NASA has invested a significant amount of money to

build the infrastructure to support these rockets.

Somewhat simpler are solid propellant rockets.   But solid

fuels have drawbacks too.  Not all solid fuels are more

stable than common liquid fuels.  For example black

powder, which is a sulfur and potassium nitrate

compound, was commonly used by cannons and some

firearms up through the twenty-first century and is still

in use in some specialized applications by militaries

around the world.  But black powder is definitely not as

stable as gasoline.  If I take some gasoline and shake it

or hit it, I’m not going to have a problem.   But if I hit a

small pile of black powder with a hammer bad things can

happen.   Solid fuels are also more difficult to transport

throughout the vehicle.  The vehicle’s fuel storage, the

gas tank, the fuel lines, fuel pump and

carburetor/injectors form a fairly simple and dependable

system of fuel distribution to the engine.  Some engines

had been built using powdered solid fuels, but they’re not

in common use.   Liquid fuels are just easier to use - -

just much more convenient.  It’s also a little hard to turn

off that bottle rocket of a car at a stoplight.  One solid

rockets are lit they tend to turn until the fuel is gone.

Another resource:

http://www.gm.com/company/gmability/edu_k-12/5-8/index.html

National Science Standards

-All students should develop abilities necessary to do scientific

inquiry and understandings about scientific inquiry.

-All students should develop an understanding of properties and

changes of properties in matter, motions and forces and

transfer of energy.

-All students should develop abilities of technological design and

understandings about science and technology.

-All students should develop understanding of science and

technology in society.

Teacher Lesson Plans

Lab Activity: Students will design a self-propelled car

45 minutes

Teaser Activity:   Auto manufacturers have to design vehicles for different performance characteristics or parameters (safety, economy,

acceleration, endurance). Today’s lab gives you the chance to design a vehicle to compete to see which is fastest over a designated distance and which can travel the greatest distance in a given time.

Student expectations: With the materials provided, each group of

students will design a self-propelled vehicle and demonstrate their

design based upon distance and time

Teaser: Which category would your group prefer to win and why?

Using the car designed by your group measure the distance traveled by the vehicle and time taken for a specific distance and then calculate the speed. Plan on at least 3 trials

Materials List

Springs			Rubber bands

Carbon dioxide		Water bottles

Balsa wood			Wheels

Axles				Eye screws

Braided thin rope		Coping saw

Glue				Sanding block

Measuring tape

Student Worksheets

Name________________________  Vehicle design

Names of others in your lab group ____________________

______________________________________________

- Design a vehicle.  Before constructing the vehicle, draw a diagram and/or write a description of your design.

- List the materials used in your design

- Record the results of your car

- What were the design characteristics of speed and endurance in vehicle designs?

- Describe what would be optimum car characteristics for

you.   How might it be achieved?

ASSESSMENT/MASTERY CHECK:

Name ________________________________     	Quiz   self-propelled cars

According to accident scene investigator, Rolin Barrett, “we have to be careful  when we try to design a vehicle that is a best of all situations such as the fastest, covers the greatest distance, safest, etc. Because frequently the compromise will give a vehicle that will do none of these very well.  So we want to focus on the area that is most important to us.  If it happens to be speed or distance then we need to focus on one and not so much focus on the other.

1)	  If you were going to focus your design on creating a vehicle that would travel

the greatest distance, what are some design features you would include?

2)           If you were going to focus your design on creating a vehicle that would be the

fastest over a short distance, what are some design features you would include?

-If you were to create your design again, what would you change and why?

Interdisciplinary Lessons:

Math – determine the circumference of circular shapes